## Slide 1: All You Never Wanted to Know About GLP and GMP

## Slide 2: Research
By FDA standards . . .
  A VERY uncontrolled, undisciplined activity!!!
Note: Innovation is the key.

## Slide 3: Development
By comparison . . .
Much more disciplined.
GLP and cGMP become considerations.

## Slide 4: Manufacturing
Must be even more disciplined . . .
cGMP takes priority
QC becomes an important driver!

## Slide 5: What is the intent of regulations?
Provide assurance of identity, quality, and strength of pharmaceuticals.
Assure that correct procedures have been followed.
Provide documentation, traceability.
Overall Intent: To assure Quality is “built in” to the approach.

## Slide 6: What is Quality?
The ability to consistently produce the same product to meet the same specifications time after time!
Stronger, purer, higher assay, or higher yield . . . is not better!

## Slide 7: GLP and GMP
GMP:
  Protect the integrity and quality of manufactured product intended for human use.
GLP:
  Protect the integrity and quality of laboratory data used to support a product application.

## Slide 8: Current Good Manufacturing Practices (GMP or cGMP)
Must be both current and good!
Apply to all aspects of preparation when a drug entity is intended for use in humans (or target animal for animal drug).
Do not apply when drug is in Pre-Clinical Trials (animal testing).

## Slide 9
Good Laboratory Practices (GLP)
Apply when a non-clinical laboratory study (e.g. Pre-Clinical animal testing) is intended to support an application for an FDA-regulated product.

## Slide 10
Good Laboratory Practices
Title 21 CFR:
  Part 58: “ . . . For Non-Clinical Laboratory Studies”

## Slide 11
Part 58: Non-Clinical Laboratory Studies
Subpart A: General Provisions
Subpart B: Organization and Personnel
Subpart C: Facilities
Subpart D: Equipment
Subpart E: Testing Facilities Operation
Subpart F: Test and Control Articles
Subpart G: Protocol for and Conduct of a Non-Clinical Laboratory Study
Subpart H: [Reserved]
Subpart I: [Reserved]
Subpart J: Records and Reports
Subpart K: Disqualification of Testing Facilities

## Slide 12
Organization and Personnel
58.29 Personnel
(a)“Each individual engaged in the conduct of or responsible for the supervision of a nonclinical laboratory study shall have education, training, and experience, or combination thereof, to enable that individual to perform the assigned functions.”
(b)“Each testing facility shall maintain a current summary of training and experience and job description for each individual engaged in or supervising the conduct of a nonclinical laboratory study.”

## Slide 13
Organization and Personnel
Three Key Responsibilities:
  Testing Facility Management
  Study Director
  Quality Assurance Unit

## Slide 14
Organization and Personnel
58.33 Study Director
“For each nonclinical laboratory study, a scientist or other professional of appropriate education, training, and experience, or combination thereof, shall be identified as the study director. The study director has overall responsibility for the technical conduct of the study, as well as for the interpretation, analysis, documentation, and reporting of results, and represents the single point of study control.”

## Slide 15
Organization and Personnel
58.35 Quality Assurance Unit
“A testing facility shall have a quality assurance unit which shall be responsible for monitoring each study to assure management that the facilities, equipment, personnel, methods, practices, records, and controls are in conformance with the regulations in this part. For any given study, the quality assurance unit shall be entirely separate from and independent of the personnel engaged in the direction and conduct of that study.”

## Slide 16
Facilities
58.41 General
“Each testing facility shall be of suitable size and construction to facilitate the proper conduct of nonclinical laboratory studies. It shall be designed so that there is a degree of separation that will prevent any function or activity from having an adverse effect on the study.”
  Animal care facilities
  Animal supply facilities
  Facilities for handling test and control articles
  Laboratory operation areas
  Specimen and data storage facilities

## Slide 17
Equipment
58.61 Equipment Design
  “Equipment used in ... shall be of appropriate design and adequate capacity ...”
58.63 Maintenance and Calibration
  (b) “The written standard operating procedures ...”
  (c) “Written records shall be maintained ...”

## Slide 18
Testing Facilities Operation
58.81 Standard Operating Procedures
  (a) “A testing facility shall have standard operating procedures in writing setting forth nonclinical laboratory study methods ... to insure the quality and integrity of the data generated ...”
58.90 Animal Care
  (e) “Animals of different species shall be housed in separate rooms when necessary. Animals of the same species, but used in different studies, should not ordinarily be housed in the same room when inadvertent exposure to control or test articles or animal mix-up could affect the outcome of either study. If such mixed housing is necessary, adequate differentiation by space and identification shall be made.”

## Slide 19
Test and Control Articles
58.105 Test and Control Article Characterization
  (a) “The identity, strength, purity, and composition which appropriately define the test or control article shall be determined for each batch and shall be documented.”
  (b) “The stability of each test or control article shall be determined ...”

## Slide 20
Protocol for Conduct of a Nonclinical Laboratory Study
58.120 Protocol
  (a) “Each study shall have an approved written protocol that clearly indicates the objectives and all methods for the conduct of the study.”
58.130 Conduct of a Non-clinical Laboratory Study
  (a) “The nonclinical laboratory study shall be conducted in accordance with the protocol”

## Slide 21
Records and Reports
58.185 Reporting of Non-clinical Laboratory Study Results
  (a) “A final report shall be prepared for each nonclinical laboratory study ...”
58.190 Storage and Retrieval of Records and Data
  (a) “All raw data, documentation, protocols, final reports, and specimens ... shall be retained.”

## Slide 22: Current Good Manufacturing Practices
Title 21 CFR:
  Part 210: “ . . . In Manufacturing, Processing, Packing, or Holding of Drugs; General”
  Part 211: “ for Finished Pharmaceuticals”
  Part 600: Biologics
  Part 820: Medical Devices

## Slide 23: Part 210: General Provisions
210.1 (a) “The regulations set forth in this part and in parts 211 through 226 of this chapter contain the minimum current good manufacturing practice for methods to be used in, and the facilities or controls to be used for, the manufacture, processing, packing, or holding of a drug to assure that such drug meets the requirements of the act as to safety, and has the identity and strength and meets the quality and purity characteristics that it purports or is represented to possess.”

## Slide 24: Part 210: General Provisions
210.1 (b) “The failure to comply with any regulation set forth ... in the manufacture, processing, packing, or holding of a drug shall render such drug to be adulterated under section 501(a)(2)(B) of the act and such drug, as well as the person who is responsible for the failure to comply, shall be subject to regulatory action.”

## Slide 25: Part 211: Finished Pharmaceuticals
Subpart A: General Provisions
Subpart B: Organization and Personnel*
Subpart C: Buildings and Facilities*
Subpart D: Equipment*
Subpart E: Control of Components and Drug Product Containers and Closures*
Subpart F: Production and Process Controls*
Subpart G: Packaging and Labeling Control
Subpart H: Holding and Distribution
Subpart I: Laboratory Controls*
Subpart J: Records and Reports*
Subpart K: Returned and Salvaged Drug Products

## Slide 26: Organization and Personnel
211.22 (a) Responsibilities of the Quality Control Unit “There shall be a quality control unit that shall have the responsibility to approve or reject all ...”
211.25 (a) Personnel Qualifications “Each person engaged in the manufacture, processing, packing, or holding of a drug product shall have education, training, and experience, or any combination thereof, to enable that person to perform the assigned functions. Training shall be ...”
211.28 Personnel responsibilities
211.34 Consultants

## Slide 27: Buildings and Facilities
211.42 Design and Construction Features
(a) “Any building or buildings used in the manufacture, processing, packing, or holding of a drug product shall be of suitable size, construction, and location to facilitate cleaning, maintenance, and proper operation.”
211.46 Ventilation, Air Filtration, Air Heating and Cooling
(b) “Equipment for adequate control over air pressure, micro-organisms, dust, humidity, and temperature shall be provided when appropriate for the manufacture, processing, packing, or holding of a drug product.”

## Slide 28: Buildings and Facilities
211.46 (continued)
(d) “Air-handling systems for ... penicillin shall be completely separate from those for other drug products for human use.”
Other Issues:
  211.44 Lighting
  211.48 Plumbing
  211.50 Sewage and refuse
  211.52 Washing and toilet facilities
  211.56 Sanitation
  211.58 Maintenance

## Slide 29: Equipment
211.63 Equipment Design, Size, and Location “Equipment used in the manufacture, processing, packing, or holding of a drug product shall be of appropriate design, adequate size, and suitably located to facilitate operations for its intended use and for its cleaning and maintenance.”
211.65 Equipment Construction
211.67 Equipment Cleaning and Maintenance (a) “Equipment and utensils shall be cleaned, maintained, and sanitized at appropriate intervals ...” (b) “Written procedures shall be established and followed...” (c) “Records shall be kept ...”

## Slide 30: Equipment
211.68 Automatic, Mechanical, and Electronic Equipment (a) “... including computers ... may be used. If such equipment is used, it shall be routinely calibrated, inspected, or checked according to a written program designed to assure proper performance. Written records of those calibration checks and inspections shall be maintained.”
(b) “Appropriate controls shall be exercised over computer or related systems to assure that changes ... are instituted only by authorized personnel.”
211.72 Filters

## Slide 31: Control of Components and Drug Product Containers and Closures
211.80 General Requirements
(a) “There shall be written procedures describing in sufficient detail the receipt, identification, storage, handling, sampling, testing, and approval or rejection of components and drug product containers and closures; such written procedures shall be followed.”
211.82 Receipt and Storage: (a) “Upon receipt ... shall be examined visually ...” (b) “... shall be stored under quarantine until they have been tested or examined, as appropriate, and released.”

## Slide 32: Control of Components and Drug Product Containers and Closures
211.84 Testing and Approval or Rejection (a) “Each lot ... shall be withheld from use until the lot has been sampled, tested or examined, as appropriate, and released for use by the quality control unit.” (b) “Representative samples ... of each lot shall be collected ...” (d) “Samples shall be examined and tested as follows ...”
  “At least one test ... to verify identity.”
  “... for conformity with all appropriate written specifications for purity, strength, and quality”
(e) “Any lot ... that meets ... specifications [by testing according to paragraph (d)] may be approved and released for use.”

## Slide 33: Control of Components and Drug Product Containers and Closures
211.86 Use of Approved [Stock]
“... the oldest approved stock is used first.”
211.87 Retesting of approved [stock]
211.89 Rejected [Stock] “Rejected [stock] shall be ... controlled ... to prevent their use ...”
211.94 Drug Product Containers and Closures: (a) “... shall not be reactive, additive, or absorptive ...” (b) “... shall provide adequate protection ...” (c) “... shall be clean and ...”

## Slide 34: Production and Process Controls
211.100 Written Procedures; Deviations (a) “There shall be written procedures for production and process control ...” (b) “Written production and process control procedures shall be followed ...”
211.101 Charge-in of Components Note important detail! (d) “Each component shall be added to the batch by one person and verified by a second person.”
211.103 Calculation of Yield

## Slide 35: Production and Process Controls
211.105 Equipment Identification (a) “[Equipment] shall be properly identified at all times to indicate their contents and, when necessary, the phase of processing of the batch.” (b) “[Equipment] shall be identified by a distinctive identification number or code ...”
211.110 Sampling and Testing of In-Process Materials and Drug Products
211.111 Time Limitations on Production

## Slide 36: Production and Process Controls
211.113 Control of Microbiological Contamination (a) for non-sterile drugs (b) for sterile drugs
211.115 Reprocessing (a) “Written procedures shall be established and followed ...” (b) “... review and approval of the quality control unit.”

## Slide 37: Packaging and Labeling Control
211.122 Materials Examination and Usage Criteria (a) “There shall be written procedures ...” (c) “Records shall be kept ...” (d) “Labels and other labeling materials for each different drug product, strength, dosage form, or quantity of contents ...”
211.125 Labeling Issuance (a) “Strict control shall be exercised over labeling issued for use in drug product labeling operations.” (c) “Procedures shall be used to reconcile the quantities of labeling issued, used, and returned ...”

## Slide 38: Packaging and Labeling Control
211.130 Packaging and Labeling Operations “There shall be written procedures designed to assure that correct labels, labeling, and packaging materials are used for drug products; such written procedures shall be followed.”
211.137 Expiration Dating “To assure that a drug product meets applicable standards of identity, strength, quality, and purity at the time of use, it shall bear an expiration date determined by appropriate stability testing ...”

## Slide 39: Holding and Distribution
211.142 Warehousing Procedures “Written procedures ... shall be established and followed. They shall include: (a) Quarantine of drug products before release by the quality control unit. (b) Storage of drug products under appropriate conditions ...”
211.150 Distribution Procedures “Written procedures shall be established and followed. They shall include: (a) ... the oldest approved stock ... is distributed first. (b) ... the distribution of each lot of drug product can be readily determined to facilitate its recall if necessary.”

## Slide 40: Laboratory Controls
211.160 General Requirements
(a) “The establishment of any specifications, standards, sampling plans, test procedures, or other laboratory control mechanisms required by this subpart, including any change in such ..., shall be drafted by the appropriate organizational unit and reviewed and approved by the quality control unit. The requirements in this subpart shall be followed and shall be documented at the time of performance. Any deviation ... shall be recorded and justified.”

## Slide 41: Laboratory Controls
211.160 (continued)
(b) “Laboratory controls shall include the establishment of scientifically sound and appropriate specifications, standards, sampling plans, and test procedures designed to assure that components, drug product containers, closures, in-process materials, labeling, and drug products conform to appropriate standards of identity, strength, quality, and purity.” Note subpart (4): “The calibration of instruments, apparatus, gauges, and recording devices at suitable intervals in accordance with an established written program ...”

## Slide 42: Laboratory Controls
211.165 Testing and Release for Distribution (a) “For each drug product, there shall be appropriate laboratory determination of satisfactory conformance to final specifications for the drug product ...” (e) “The accuracy, sensitivity, specificity, and reproducibility of test methods employed by the firm shall be established and documented [validated].”

## Slide 43: Laboratory Controls
211.166 Stability Testing “There shall be a written testing program designed to assess the stability characteristics of drug products. The results of such stability testing shall be used in determining appropriate storage conditions and expiration dates.”
211.167 Special Testing Requirements
  (a) sterile and/or pyrogen-free products
  (b) ophthalmic products
  (c) controlled release products
211.168 Reserve Samples

## Slide 44: Laboratory Controls
211.176 Penicillin Contamination “If a reasonable possibility exists that a non-penicillin drug product has been exposed to cross-contamination with penicillin, the non-penicillin drug product shall be tested for the presence of penicillin. Such drug product shall not be marketed if detectable levels are found when tested according to procedures specified ...”

## Slide 45: Records and Reports
211.180 General Requirements (a) and (b) Any written records “shall be retained for at least 1 year after the expiration date ... or 3 years after distribution ...” (c) “... shall be readily available for authorized inspection during the retention period at the establishment where the activities ... occurred.” (e) “... shall be maintained so that data therein can be used for evaluating, at least annually, the quality standards of each drug product to determine the need for changes in ... specifications or manufacturing or control procedures. Written procedures shall be established and followed for such evaluations ...”

## Slide 46: Records and Reports
211.182 Equipment Cleaning and Use Log “A written record of major equipment cleaning, maintenance, and use ...”
211.184 Component, Drug Product Container, Closure, and Labeling Records (a) “The identity and quantity of each shipment of each lot ...” (b) “The results of any test or evaluation performed ...” (c) “An individual inventory record ... and ... a reconciliation of the use ...” (d) “Documentation of the examination and review of labels ...” (e) “The disposition of rejected ...”

## Slide 47: Records and Reports
211.186 Master Production and Control Records “To assure the uniformity from batch to batch, master production and control records for each drug product, including ... The preparation of master production and control records shall be described in a written procedure and such written procedure shall be followed.”
211.188 Batch Production and Control Records “Batch production and control records shall be prepared for each batch of drug product produced and shall include complete information relating to the production and control of each batch.”

## Slide 48: Records and Reports
211.192 Production Record Review “All drug product production and control records, including those for packaging and labeling, shall be reviewed and approved by the quality control unit to determine compliance with all established, approved written procedures before a batch is released or distributed. Any unexplained discrepancy ... or the failure of a batch or any of its components to meet any of its specifications shall be thoroughly investigated. The investigation shall extend to other batches ... that may have been associated with the specific failure or discrepancy. A written record of the investigation shall be made and shall include the conclusions and follow-up.”

## Slide 49: Records and Reports
211.194 Laboratory Records (a) “complete data derived from all tests … (b) “any modification of an established method [including] the reason for the modification and data to verify that ... results are at least as accurate and reliable ... as the established method. (c) “any testing and standardization of laboratory reference standards, reagents, and standard solutions. (d) “... periodic calibration of laboratory instruments [etc.]. (e) “... stability testing.”

## Slide 50: Records and Reports
211.196 Distribution Records “... shall contain the name and strength of the product and description of the dosage form, name and address of the consignee, date and quantity shipped, and lot or control number of the drug product.”

## Slide 51: Records and Reports
211.198 Complaint Files (a) “Written procedures describing the handling of all written and oral complaints regarding a drug product shall be established and followed. Such procedures shall include provisions for review by the quality control unit of any complaint involving the possible failure of a drug product to meet any of its specifications and ... a determination as to the need for an investigation. Such procedures shall include provisions for review to determine whether the compliant represents a serious and unexpected adverse drug experience which is required to be reported to the FDA.” (b) “A written record of each complaint shall be maintained in a file ...”

## Slide 52: Returned and Salvaged Drug Products
211.204 Returned Drug Products “... shall be identified as such and held. If the conditions ... cast doubt on the ... drug product, [it] shall be destroyed unless examination, testing, or other investigations prove [it] meets appropriate standards ... Records of returned drug products shall be maintained and shall include ... the reason for the return ...”
211.208 Drug Product Salvaging “Drug products that have been subjected to improper storage conditions ... shall not be salvaged and returned to the marketplace. Whenever there is a question ... salvaging operations may be conducted only if there is evidence ...”

## Slide 53: What Does It All Mean
Documentation System:
Written procedures (SOPs) must be available for all operations and activities from receipt of raw materials to shipment and distribution of finished goods.
SOPs must be followed.
Records must be kept (of everything!)
Also:
Facilities must be appropriate and provide an acceptable environment to protect product from contamination.
Equipment must be kept clean and well maintained.

## Slide 54
Important Documents
Standard Operating Procedure (SOP): A document that describes a routine procedure of general use which is not specific to one product.
Master Production and Control Record (MPCR): A document that describes the procedure for the preparation of a specific product.
Batch Production and Control Record (BPCR): An exact copy of the approved MPCR issued for each production batch to record the data for that particular batch.

## Slide 55: Bottom Line
Document, Document, Document!!!
In FDA-speak:
  “If it is not documented . . .
        it did not happen!”
        or, it’s a rumor!”